## Slide 1
KAVACH
Intelligent Vehicle Safety System
Detect. Alert. Respond. Automatically.
7 Sensors
4 Alert Levels
< ₹1500
Team COREsentinel | Anwesha Mohanty · Ariana Mohanty · Ashutosh Mishra
v2.0
ESP32
Based
WiFi
Enabled
< ₹1500

## Slide 2
THE PROBLEM
India recorded 1.8 lakh road deaths in 2024 — highest ever. Odisha alone: 700+ bus injuries (2022–24).
Driver Fatigue
Microsleep & sudden unconsciousness
Engine Failure
Overheating & gas leaks
Collision Risk
Blind spots & unseen obstacles
No Crash Alert
Zero post-impact notification
No SOS System
No auto-alert to authorities
No Indian public bus has a real-time, multi-parameter safety system today.

## Slide 3
WHAT IS KAVACH?
A low-cost ESP32-based vehicle safety system that uses 7 sensors to watch the bus every 500ms — automatically warning, alerting, cutting the engine, and calling for help.
01
Detect Before It Happens
500ms continuous sensor scan
02
No False Alarms
Only sensor combinations trigger critical alerts
03
Graduated Alerts
L1 Caution → L2 Warning → L3 Critical → L4 Emergency
04
Auto Emergency Response
ESP32 WiFi SOS with Bus ID if no response in 5s
05
Affordable & Scalable
Under ₹1500 — fits any OSRTC, school or private bus

## Slide 4
COMPONENTS
ESP32
Microcontroller + WiFi
Brain + SOS sender
HC-SR04
Ultrasonic Sensor
Obstacle distance
PIR Sensor
Motion Sensor
Driver presence
DHT11
Temp & Humidity
Cabin temperature
MQ-7 / MQ-135
Gas Sensor
CO / air quality
Vibration Sensor
Impact Sensor
Crash detection
Sound Sensor
Microphone Module
Cabin silence / microsleep
IR Sensor
Infrared Sensor
Door open / blind spot
16×2 LCD I2C
Display
Alert messages
Buzzer
Audio Output
3 alarm patterns
Relay Module
Actuator
Cuts ignition at L3
LEDs ×3
Visual Output
Green / Yellow / Red

## Slide 5
SYSTEM ARCHITECTURE
SENSORS (INPUT)
HC-SR04 (Distance)
PIR Sensor (Presence)
DHT11 (Temperature)
MQ-7/135 (Gas/CO)
Vibration (Crash)
Sound (Silence)
IR Sensor (Blind Spot)
→
CONTROLLER
ESP32
KAVACH Fusion Engine
• Reads sensors every 500ms
• Applies fusion logic
• Decides alert level L1–L4
• Active 24/7
→
OUTPUTS
16×2 LCD
Text alerts
Buzzer
3-level alarm
Relay Module
Ignition cutoff
ESP32 WiFi
SOS to authorities
LEDs ×3
Status lights

## Slide 6
SENSOR FUSION LOGIC
No single sensor triggers a critical alert — only dangerous combinations do.
MQ-7 HIGH + DHT11 > 50°C
Gas + Heat = Engine Fire
Level 3 — Relay OFF + Alarm
PIR ABSENT + HC-SR04 < 20cm
No Driver + Obstacle = Collision
Level 3 — Relay OFF + Alarm
Vibration Spike + PIR No Motion
Physical Impact = Crash
Level 3 → Level 4 WiFi SOS
PIR Absent + Sound Silent
No Driver + Silence = Microsleep
Level 2 — Warning + Escalates
MQ-7 HIGH alone
CO Leak — Single Sensor
Level 2 — Rhythmic Beep
HC-SR04 < 80cm alone
Obstacle Nearby — Low Risk
Level 1 — Single Beep every 3s

## Slide 7
ALERT LEVELS
LEVEL 1
CAUTION
Trigger: Single sensor flag — obstacle < 80cm
Response: Single beep every 3s · LCD info · Green LED
LEVEL 2
WARNING
Trigger: Two-sensor combo / CO alone / Microsleep
Response: Rhythmic double beep · Yellow LED · LCD warning
LEVEL 3
CRITICAL
Trigger: Fire risk / Collision / Crash detected
Response: Continuous alarm · Red LED · Relay cuts ignition
LEVEL 4
EMERGENCY
Trigger: No human response for 5+ seconds
Response: ESP32 sends WiFi SOS with Bus ID to authorities

## Slide 8
ESP32 PIN CONNECTIONS
GPIO 4
→
DHT11
DATA
GPIO 5
→
HC-SR04
TRIG
GPIO 12
→
LED Yellow
Anode
GPIO 13
→
Buzzer
+
GPIO 18
→
HC-SR04
ECHO
GPIO 19
→
PIR Sensor
OUT
GPIO 21
→
LCD I2C
SDA
GPIO 22
→
LCD I2C
SCL
GPIO 25
→
LED Green
Anode
GPIO 26
→
Relay Module
IN
GPIO 27
→
LED Red
Anode
GPIO 32
→
Sound Sensor
DO
GPIO 33
→
IR Sensor
OUT
GPIO 34
→
MQ-7 / MQ-135
AO
GPIO 35
→
Vibration
DO
⚡ VIN → All sensor VCC | GND → All sensor GND | 10kΩ on DHT11 DATA | 220Ω on each LED

## Slide 9
LIVE EMERGENCY NOTIFICATION
When Level 4 triggers — ESP32 instantly sends a Telegram alert to authorities.
Level 3
Triggers
→
5s No
Response
→
ESP32
Sends SOS
→
Telegram
Notification
Telegram — KavachAlertBot
🚨 KAVACH EMERGENCY ALERT 🚨 Bus ID : OSRTC-BUS-07 Alert : CRASH DETECTED Status : No response for 5 seconds Action : Ignition cut. Help needed!
— KAVACH v2.0 Auto Alert

## Slide 10
KAVACH
Detect · Alert · Respond · Automatically
7
Sensors
4
Alert Levels
< ₹1500
Per Vehicle
Team COREsentinel | OUTR | Anwesha Mohanty · Ariana Mohanty · Ashutosh Mishra